## Slide 1: CompTIA Network +
Chapter 2
Dissecting the OSI Model

## Slide 2: Objectives
What is the purpose of a Network model?
What are the layers of the OSI model?
What are the characteristics of each layer of the OSI model?
How does the TCP/IP stack compare to the OSI model?
What are the well-known TCP and/or UDP port numbers for a given collection of common applications

## Slide 3: The Purpose of Reference Models
It breaks network communication into smaller, simpler parts that are easier to develop.
It facilitates standardization of network components to allow multiple-vendor development and support.
It allows different types of network hardware and software to communicate with each other.
It prevents changes in one layer from affecting the other layers so that they can develop more quickly.
It breaks network communication into smaller parts to make learning it easier to understand.

## Slide 4: Warriors of the Net

## Slide 5
The OSI seven-layer model
Application
Presentation
Session
Transport
Network
Data Link
Physical
Figure 2-2 OSI Stack
1
2
3
4
5
6
7

## Slide 6: Mnemonics for the OSI Model
  Away
  Pizza
  Sausage
  Throw
  Not
  Do
  Please
  All
  People
  Seem
  To
  Need
  Data
  Processing

## Slide 7: Protocol Data Unit (PDU)
Application
Presentation
Session
Transport
Network
Data Link
Physical
Segments
Packets
Frames
Bits
Figure 2-3 PDU Names

## Slide 8: Quick Summary of Layers 1-4
Transport
Network
Data Link
Physical
1
2
3
4
TCP & UDP Ports
Routers, IP Address
Switches, MAC Address
Cables
Service
WAN
LAN

## Slide 9: OSI Layers in Wireshark
1
2
3
4
7

## Slide 10: Physical Layer
Application
Presentation
Session
Transport
Network
Data Link
Physical
How Bits are represented on the medium
Wring standards for connectors and jacks
Physical topology
Synchronizing bits
Bandwidth usage
Multiplexing strategy
Figure 2-4 Layer 1: Physical Layer

## Slide 11: Wiring Standards

## Slide 12: Asynchronous and Synchronous Communications
Synchronizing Bits
  Two devices must agree on when one bit stops and another bit starts
Asynchronous
  Uses start and stop bits
Synchronous
  Internal clocks are synchronized at each end of the cable

## Slide 13: Bandwidth Usage
Broadband
  Multiple channels share the same medium
  Ex: cable TV uses frequency division multiplexing (each channel uses a different frequency range)
Baseband
  The whole medium is used for one transmission
  Example: Ethernet

## Slide 14: Time-Division Multiplexing (TDM)
ABCA_CABCA_C
Each channel gets the same amount of time on the wire
AAAA
B_B_
CCCC

## Slide 15: Statistical Time-Division Multiplexing (StatTDM)
ABCACABCAC
AAAA
B_B_
CCCC
Busy channels get more time on the wire

## Slide 16: Frequency Division Multiplexing (FDM)
AAAA
B_B_
CCCC
Example: signals sent with different colors through the same fiber optic cable
AAAA
B_B_
CCCC
AAAA
B_B_

## Slide 17: Layer 1 Devices
Cables
Wireless access points
Hubs
  Because they don’t pay any attention to addresses, they just deliver signals to every connected device like a crossover cable

## Slide 18: Data Link Layer
Data Link
Application
Presentation
Session
Transport
Network
Physical
Physical Addressing
Logical topology
Method of transmitting on the media
Figure 2-8 Layer 2: The Data Link Layer
MAC
LLC
Connection Services
Synchronizing transmissions

## Slide 19: MAC Addresses
IPCONFIG /ALL
Physical Address
Built into the network interface

## Slide 20: Connection Services
Flow control
  Prevents sender from sending data faster than the client can accept it
Error control
  When a frame is received, a checksum is used to detect errors
    Usually a Cyclic Redundancy Check (CRC)
  If the receiver's checksum does not match the sender's checksum, the frame is discarded and resent

## Slide 21: Layer 2 Devices
Switches
Bridges
Network Interface Cards (NICs)

## Slide 22: Network Layer
Network
Data Link
Application
Presentation
Session
Transport
Physical
Logical addressing
Switching
Route discovery and selection
Connection services
Bandwidth usage
Multiplexing strategy
Figure 2-9 Layer 3: The Network Layer

## Slide 23: IP Address
Logical address
Changes when the device is moved

## Slide 24: Switching
Packet switching
  Data is broken into packets
  Many packets travel along network connections like cars on a freeway
Circuit switching
  A physical line is dedicated to each connection
  Ex: old copper landline phone systems
Message switching
  Store-and-forward, like email

## Slide 25: Layer 3 Devices
Routers
Multilayer Switches

## Slide 26: Transport Layer
Transport
Network
Data Link
Application
Presentation
Session
Physical
TCP/UDP
Windowing
Buffering
Figure 2-10 Layer 4: The Transport Layer

## Slide 27: TCP and UDP
Transmission Control Protocol (TCP)
  Connection-oriented and reliable
  Handshake makes sure both ends are ready
  Segments are acknowledged and resent if necessary
User Datagram Protocol (UDP)
  Connectionless and unreliable
  No handshake
  Best-effort delivery, no acknowledgements

## Slide 28: TCP Sliding Window
Figure 2-11 TCP Sliding Window

## Slide 29: ICMP (Internet Control Message Protocol)
At layer 4
Used by ping and traceroute, and to indicate errors such as dropped packets

## Slide 30: Session Layer
Session
Transport
Network
Data Link
Application
Presentation
Physical
Setting up a session
Maintaining a session
Tearing down a session
Figure 2-12 Layer 5: The Session Layer

## Slide 31: Example of a Session
User logs in with a username & password
All data now has a special significance until that user logs off, or the session times out, or is terminated some other way
Layer 6 Protocol
  H.323 (voice or video)
  NetBIOS (file sharing)

## Slide 32: Presentation Layer
Presentation
Session
Transport
Network
Data Link
Application
Physical
Data formatting
Encryption
Figure 2-13 Layer 6: The Presentation Layer

## Slide 33: Application Layer
Application
Presentation
Session
Transport
Network
Data Link
Physical
Application services
Service advertisement

## Slide 34: Application Layer
Closest to the user
Hands data to an application in the format it expects, with no addresses or other transmission artifacts
Examples: a downloaded file, an email message

## Slide 35: The TCP/IP Stack
Application
Transport
Internet
Network Interface

## Slide 36: The TCP/IP and OSI Models Compared
Application
Transport
Internet
Network Interface
TCP/IP Stack
Application
Presentation
Session
Transport
Network
Data Link
Physical
OSI Stack
Figure 2-15 TCP/IP Stack

## Slide 37: IP Ver4 Header

## Slide 38: TTL (Time-to-Live)
TTL decreases by one each time the packet is forwarded by a router
If TTL reaches zero, the packet is discarded
This eliminates packets trapped in routing loops

## Slide 39: Demo: Routing Loop

## Slide 40: TCP Header
Figure 2-17 TCP Segment Format

## Slide 41: TCP Header Fields
Port numbers
  Indicate which program on the end device should receive the data
  Examples: Port 25 for email, 80 for HTTP
Window size
  Number of bytes that can be sent before waiting for an ACK

## Slide 42: TCP Header Fields
Sequence and Acknowledgement numbers
  Used to put packets in order to reassemble files and other large messages
Flags like SYN and ACK are used for the TCP handshake and to acknowledge data received

## Slide 43: UDP Header
0 | 16 |  | 31
SOURCE PORT |  | DESTINATION PORT | 
LENGTH |  | CHECKSUM | 
No handshake, acknowledgements, sequencing, or flow control

## Slide 44: Common Ports Link Ch 2d for flash cards

## Slide 45: Port Types
Port numbers are assigned in various ways, based on three ranges:
System Ports (0-1023), System Ports are assigned by IETF process for standards-track protocols, as per RFC6335. Also known as well-known-ports
User Ports (1024-49151) ,User Ports are assigned by IANA using the "Expert Review" process, as per RFC6335
Dynamic and/or Private Ports (49152-65535), Dynamic Ports are not assigned, they are dynamically created as your computer need them. Also known as ephemeral ports.

## Slide 46: Communication Between Two Systems